## Slide 1: API & Developer Tools
Introduction
October 2017

## Slide 3: Introduction
The Test SLATE Application Programming Interface (API) was developed for Test SLATE Version 12 and is supported in all later versions. It is a long term solution for a Test SLATE API that includes expanded functionality, easier development, and better API documentation.
Powerful tools for Developers
Supports development of Custom Data Source Plug-ins

## Slide 4
LabVIEW Integration Tools
  API &Palettes
  Create Project
Data Source Template
  Main Menu Additions
  System Explorer Nodes
  SubSystem Level Editor
  Configuration Level Editor
  Source Run-Time
  Build Scripts and Specifications

## Slide 5: Test SLATE API
LabVIEW Integration Overview

## Slide 6: LabVIEW Integration – API & Palettes
Test SLATE API
  Test SLATE.lvlib Library added to vi.lib
  Contains interface code for Test SLATE
  Integrated into LabVIEW Functions Palette

## Slide 7: CVT Palette
Current Value Table access (All or by Data Type)
Data and Conversion Information
Index Information provided by Tag Index and Type Info.vi

## Slide 8: Data Storage Palette
Current Group and Burst Status
Source communication to Circular Buffers

## Slide 9: Message & Error Palette
Communicate to the Message Log
  Send Message
  Error Handling
Source Commands
  Stop, Calibrate, Reload, etc

## Slide 10: Source Object Palette
Source Objects contain Source settings
  Source Name, Channel Types, CVT Index, Data Storage Settings
  Use Initialize function to create
    Automatically generated when using the Template

## Slide 11: Tag Object Palette
Tag Objects contain Tag specific settings
  Name, Status, TagID, Channel ID, Sensor, etc
  Use Initialize function to create
    Automatically generated when using the Template

## Slide 12: Executive Palette
Tools commonly needed by Sources during RunTime.
Supports the Template
Includes Source Status, Time Tag Interfaces, and Source Error Handling

## Slide 13: Application Palette
Contains global information about Test SLATE
  Runset and Database .NET connections
  System Halt Flag and other application globals

## Slide 14: Test SLATE API Training
Source Template Overview

## Slide 15: Source Template
Automatically generates a functional C# and LabVIEW Source
  Generate from Windows Start Menu or via the LabVIEW Create Project Interface
  Programmer Reference Instructions located in the Doc folder of the Template

## Slide 16: Visual Studio Solution – Example Content
Link to Test SLATE
Add nodes to the System Explorer
Create Source Editor
Create Configuration-level Editor
Create Main Menu Items

## Slide 17: Visual Studio Solution – Example Interfaces
Version Definition
Database (including Command Delivery)
Message Log
User Permissions
Calling LabVIEW
Debugging

## Slide 18: LabVIEW Project – Example Content
Main VI (Performance Functions)
Loading and Reloading
Initialization
Data Collection and Control

## Slide 19: LabVIEW Project – Example Interfaces
Database
RunSet
Message Log
CVT
Data Storage
Time Tags
Channel Status
Source Status
Commands

## Slide 20: Build Scripts and Specifications
The individual template items include Build information
  Visual Studio Solution Build Properties
  LabVIEW Build Specification
Powershell Automated Build Scripts included
  Runs both Visual Studio and LabVIEW Builds
  Incorporates pdf Help documents to final bin
  Build.ps1 and Default.ps1

## Slide 21: Summary
Developers now have more examples and the ability to create Custom Plugins via a defined interface
As we go through the rest of the training we will spend time looking at each of these topics in more detail

## Slide 22: Test SLATE API Training
Test SLATE Interfaces
Optional Independent Functions
OPC Servers
HMI Interface
etc
Customer Independent Functions
Function #1
Function #2
Test SLATE Application Space
Test SLATE Core
Calculations
Calibrations
Communications
Configuration Tools
Data Analysis
Data Storage
Database Management
Diagnostics
Displays*
Filter, Post Point, Post Test
Health Monitoring
Licensing
Menus
Message Logging
OPC
Reflective Memory Manager
Security
Test Execution
Test Sequencing
etc
Optional Plug-Ins
NI-DAQmx
Neff 470
etc
Customer Plug-Ins
Plug-In #1
Plug-In #2

## Slide 23: System Explorer
System Configuration is performed using the System Explorer tree
Plug-Ins can add items and context menus to new and existing nodes
Nodes are added via the IPlugin interface
  Paths match the naming of the Nodes
Standard wording should be maintained
  New, Edit, Remove, Delete, Rename, Refresh
Context Menu
Node = SystemExplorer/Configuration/DAS

## Slide 24: Main Menu
Main Menu is used for general functions that are one or more of the following:
  Independent of specific Configuration Editing
  Only available at Run Time
  Global functions such as Copy, Paste, Administration, and Help
To programmatically add:
  Inherit from the MenuPlugIn
  Set your parentMenu field to a Jacobs.TestSLATE.UX.Core.Properties.Resources.uxMenu item
Available for extension:
  Test SLATE
  Edit
  View
  Tools
  Data Analysis
  Execute
  Calibration
  Help

## Slide 25: Message Logging
The Test SLATE Message Log is only available when the MOC is up and running. APIs are available through .NET, LabVIEW, and C/C++.
.Net
  IMessageLog interface in
    Jacobs.TestSLATE.Messaging
LabVIEW
  Send Message.vi
C/C++
  Available for external applications to send messages to the log. Contact Jacobs for this interface.
Custom Message Codes can be added.

## Slide 26: Commands
TCP/IP is the command delivery method
Each process (Source, etc) is assigned a unique Process ID
  assigned arbitrarily in multiples of 10000
  defined in the TV.Mnemonics table
Function Word contains the command information
  generated based on two items: Process ID and Command ID
  Custom Command IDs can be defined
Arguments are used to pass special settings and information with a command
Function Word (I32)
Requestor ID
Source ID
Command Bytes
Argument 0
Argument N-1
Fixed-length portion
Variable-length portion

## Slide 27: Commands - Standard
Stop | Used to exit Acquire, Diagnostics, or Calibration and return to Idle Mode.
Diagnostic | Used to Exit idle mode and collect data for Diagnostics. When in this mode, the source is reserved. It will not accept commands for acquire, calibrations, etc. The Stop command is used to exit this mode.
Kill | Used to stop collecting data and enter inactive mode. Only accepted when in idle mode.
Calibrate | Used to Exit idle mode and collect data for calibration. When in this mode, the source is reserved. It will not accept commands for acquire, diagnostics, etc. The Stop command is used to exit this mode.
Reload | Used to send the Source to the INIT state.
Soft Reload | Sends a Soft Reload Command to the requested Source Names. In addition to the Sources receiving the Soft Reloads, all other Test SLATE components will be notified that new conversion information may be available.

## Slide 28: Security and User Permissions
Test SLATE security is governed by roles and users
Roles can allow access to functions using Security Options
Plug-ins can add additional Security Options at the Main Menu or System Explorer levels

## Slide 29: Status
The Health Monitor (HM) Source and Test SLATE core provide the reporting and user interface functionality for the status information
  Heartbeat Check
  Source Status
  Tag & Channel Status
Channel and Tag Reporting
  HM Sends messages to the Message Log at a one-minute interval to report that a condition is active.
  HM will also report a status cleared message upon transition to low for each bit.
  Bad Coded Tags are not monitored and reported by the Health Monitor.
  Each display will display a color that is user-specified using the Status Color Editor when a condition. The Bad Coded Status takes precedence, followed by NaN, and then each remaining status in bit order.
Each Test SLATE Source is responsible for providing its status to Test SLATE at its regular update interval.

## Slide 30: Source Status
Status | Description | LabVIEW Global Location
Heartbeat | At each Source update interval, the Source indicates that it is currently running by incrementing the heartbeat value. | Status Globals Exec.vi: Heartbeat
System Status | The current state and error status for the Source. | Status Globals Exec.vi: System Status, Health Monitor Global Exec.vi: Various
Reload Date and TIme | The last time the Source performed a load or reload. | Status Globals Exec.vi: Reload…
Number of Chassis and Tags | The number of hardware chassis and tags the Source is currently using, if applicable | Status Globals Exec.vi: # Chassis, Channel Counts

## Slide 31: System Status
Item | Description | LabVIEW Global Location
Acquiring | Source is collecting data for a specific test case. | Status Globals Exec.vi: System Status
Stopped/ Started/ Idle | Source is running and collecting data but has not been reserved for a specific task. | 
Inactive | Source is running but is not collecting any data. This mode is usually present when an error has occurred that prevents the source from entering another state. | 
Initializing | Source is reading its configuration and setting up hardware and software to prepare for data collection. | 
Calibrating | Source is collecting data for calibrations. | 
In Diagnostics | Source is collecting data for Diagnostics. | 
Message Log Communication Error | An error occurred communicating to the Message Log. | Health Monitor Global Exec.vi: MSLog Error
Excel Error | An error occurred communicating to Excel. Message Codes 20, 509, 640..645 provided to the Health Monitor Global will produce this status. | Health Monitor Global Exec.vi: Error Information.Last Error
Command Handler Error | An error occurred communicating to the MOC via the Command Handler. Message Codes 214, 600..617, 672..677 provided to the Health Monitor Global will produce this status. | Health Monitor Global Exec.vi: Error Information.Last Error
General Error | Any codes other than above provided to the Health Monitor Global. | Health Monitor Global Exec.vi: Error Information.Last Error

## Slide 32: Channel Status
Status | Description | Status Bit
Saturated | The channel has reached the maximum or minimum reading possible for the Channel. Possible Source checks for Saturation include: Comparing maximum/minimum expected Raw Data values to hardware specified values. Monitoring hardware status information for vendor-supplied saturation status Comparing user-specified Channel High Range and Low Range values to current Raw Data. The actual check used may be different for each Source and should be documented. | 0
Conversion Error | The Raw Data provided by the Source for the Tag is suspect due to: An error converting the data provided by hardware into Raw Data for Test SLATE An error generating a calculation for a Tag An error indication from a hardware or interface providing Raw Data to Test SLATE. The actual check used may be different for each Source and should be documented. | 1
In Calibration | The Tag or its Source is currently performing a calibration. This status signifies that the data may not be actual signal data, but calibration feedback values. | 2
In Diagnostic | The Tag or its Source is currently in a diagnostics mode. This status signifies that the data may not be actual signal data, but diagnostic information. | 3
Bad Coded | Users may select to Bad Code any Channel. The status is intended to denote a Channel that is either suspect or invalid. The Bad Code information should be returned to the Source via the RunSet during testing. | 4
Inactive | The Channel is not updating or is in an error condition. This is usually set when the Source is Inactive or the Channel’s current value is “Not a Number” (NaN). | 5

## Slide 33: Tag Status
Status | Description | Bit Location
Low Trip | The Tag’s value is less than the defined Low Trip level. | 0
Low Alarm | The Tag’s value is less than the defined Low Alarm level. | 1
High Alarm | The Tag’s value is greater than the defined High Alarm level. | 2
High Trip | The Tag’s value is greater than the defined High Trip level. | 3
Rate of Change Alarm | The Tag’s value has changed faster than the defined Rate of Change for Alarm. | 4
Rate of Change Trip | The Tag’s value has changed faster than the defined Rate of Change for Trip. | 5
Tag Variance Alarm | The defined Tag’s Values vary greater than the defined allowable limit for Alarm. | 16
Tag Variance Trip | The defined Tag’s Values vary greater than the defined allowable limit for Trip. | 17

## Slide 34: Current Value Table
For every Test SLATE System Rate interval, the most current sample for each tag is stored into the CVT as Counts, Millivolts, and Calibrated Engineering Units (EUD)
These values are used to
  record Log data
  check for alarms and trips
  view on Display and Diagnostic windows
Display and Diagnostic windows first convert the Calibrated EUD data to the requested Display EUD prior to display.

## Slide 35: Current Value Table
Source 1 |  |  | Source 2 |  |  | Source 3 | 
Tag 1 | Counts |  | Tag A | Millivolts |  | Tag 5 | EUD
Tag 2 |  |  | Tag B |  |  | Tag 6 | 
Tag 3 |  |  | Tag C |  |  | Tag 7 | 
Tag 4 |  |  | Tag A | EUD |  | Tag 8 | 
Tag 1 | Millivolts |  | Tag B |  |  | Tag 9 | 
Tag 2 |  |  | Tag C |  |  | Tag 10 | 
Tag 3 |  |  |  |  |  | Tag 11 | 
Tag 4 |  |  |  |  |  | Tag 12 | 
Tag 1 | EUD |  |  |  |  | Tag 13 | 
Tag 2 |  |  |  |  |  | Tag 14 | 
Tag 3 |  |  |  |  |  | Tag 15 | 
Tag 4 |  |  |  |  |  | Tag 16 | 

## Slide 36: Circular Buffer
Data is in Raw units (lowest available from Source)
Independent per Source
Timestamps per Source
Sized per Source according to Capture Rate
This buffer has filled once and has started to overwrite the oldest samples.

## Slide 37: Circular Buffer Process

## Slide 38: Test SLATE API Training
Database Basics

## Slide 39: Facility Database
Contains
  Sensor Configuration
  Calibration History
  Primary and Secondary Unit Information
Primary units are also referred to as ‘Calibration Units”. “Secondary Units” can be selected in the tag editor for display and reporting purposes; conversion factors are applied to the “Calibration Units” to convert to “Secondary Units”. This is useful for displaying temperature in Deg F for example for a device that would normally read in Deg C.
There is currently no user interface in Test SLATE for entering engineering units – they are entered directly into the Facility database using Microsoft SQL Server Management Studio.

## Slide 40: TV Database
Contains
  Source Information
  Channel and Tag Information
  Command and PC Information
  Automated Test Definitions
  Data Storage and other Settings

## Slide 41: TV Database – Source Tables
Every Source is added to the Table
  Keyed by Cell (System) and Source ID
  EUD Type determines conversions applied
    Counts, Intermediate, EUD
  Mnemonic is the type of Source.
    Must be defined in dbo.Mnemonics
  DataBufferSample Size and SourceDataRate used to determine Circular Buffer Size

## Slide 42: TV Database – Channel Tables
Every Channel is added to the Table
  Keyed by Cell (System), Channel ID, and Source ID
  EUD Type determines conversions applied
    Counts, Intermediate, EUD
  Units and Ranges are carried over to Tags
  ChannelOrder can be used to control the order of the Tags in a Configuration

## Slide 43: TV Database - Tags
Every Tag is added to the Table
  Keyed by Cell (System), Cfg ID, and Tag ID
  Source channels will also have Channel IDs defined
  Added and defined by the Tag Editor

## Slide 44: TV Database – Commands to Sources
Source Types are defined in Mnemonics table
As Sources are added individual entries are added to dbo.CmdDelProcesses
  Defaulted to Mnemonics
  Multiple instances of a Source may be invoked

## Slide 45: Test SLATE API Training
Creating a New Source

## Slide 46: General Test Information
Item | Description | Global Location
Test SLATE Path | The installation path for Test SLATE. | TestVIEW Paths Global.vi: TestVIEW Path
Data Files Path | The base path that Data Storage will use to store Data Directories. | TestVIEW Paths Global.vi: Data Files Path
Run Definition | The Run Definition name loaded. | TestVIEW Paths Global.vi: Current Test Number
Configuration Description | The description of the Configuration loaded. | TestVIEW Paths Global.vi: Test Description
Running Configuration | The name of the Configuration loaded. | TestVIEW Paths Global.vi: Running Configuration
MOC Node Name | The computer name of the MOC. | TestVIEW Paths Global.vi: Node Name
MSLog Port | The TCP/IP port at which the Message Log is listening for new messages. | MOC Message Global.vi: MSLOG Port
Cell ID | The ID in the Test SLATE database of the current System loaded. | RunSet
CfgID | The ID in the Test SLATE database of the current Configuration loaded. | RunSet
TestID | The ID in the Test SLATE database of the current Run Definition loaded. | RunSet
Source Names | Contains the list of Sources in the current test, in the order in which they will appear in all lists including Reflective Memory. | Instrument Information.vi: Source Name

## Slide 47: LabVIEW Source and Tag Classes
Objects contain RunSet information pertaining to Sources and Tags
Automatically generated by the Template for use
Source object used for most template inputs
  Replaces need for Device Index
  Contains CVT index and Data Type information
  Contains Data Storage interface information
Brown Source Object wire
simplifies interface to the
Data Storage Circular Buffers

## Slide 48: Error Cluster
Unhandled Error - Set this to true when you have an error condition. The Error Handler will set it to false once the error has been sent to the Message Log.
Error Status – Set this to true when you have an error condition.
Error Code – Enter the code for your error. The code must be listed in the message Codes.xls workbook.
Error Source – Enter the VI where the error is generated.
Severity – Select how serious the error or message is. When Emergency is selected, the user at the MOC will get a dialog box displaying the message.
Message Type – Select the type of message. Options are Code or Text. Always use Code for errors.
Number of Values – Error Handler automatically fills this in.
Msg Value Type – Enter the list of the types of values that you need to insert into the message. Options are Integer (1), Real (2), and String (3). The entries should match the order in the message.